## Slide 1: Kernel Integration

## Slide 2: Kernel Integration – how to integrate driver into the kernel – Introduction
The NFC reference stack communicates with the ST21NFCD NFC controller via the ST HAL component through the st21nfc kernel driver. The HAL uses the /dev/st21nfc device node and the read/write/poll/ioctl interfaces of this driver to manage ST21NFCD device access. The I2C communication is realized through the I2C client driver st21nfc.c. This client driver must be registered in the kernel during the board initialization.
  Note:The I2C client address of the ST21NFCD device is 0x08 by default.
The device host needs to provide 2 GPIOs in order to manage the ST21NFCD efficiently:
  • A GPIO configured as input connected to the wake-up pin of ST21NFCD, used to interrupt the NFC stack upon events on the NFC RF interface. Any GPIO pin can be used as long as it is able to generate interrupts. On the ST21NFCD side, it is a push-pull bi-directional…
  • A GPIO configured as output connected to the reset pin of ST21NFCD, used to reset the NFC microcontroller. Also any GPIO pin can be used.
  Management of those GPIOs is done inside the st21nfc kernel driver.

## Slide 3: Kernel Integration – how to integrate driver into the kernel – Configure the kernel driver with DTS
This section describes how to integrate the ST21NFC driver when your kernel supports the device tree (DTS).
1.Edit the file $KERNEL_DIR/drivers/nfc/Kconfig and add the following to include the driver:
  config NFC_ST21NFC
  bool "ST Microelectronics ST21NFC NFC Controller Driver"
  depends on I2C
  help
  ST Microelectronics ST21NFC Near Field Communication controller support.
2. Edit the file $KERNEL_DIR/drivers/nfc/Makefile and add the following to compile the driver code:
  obj-$(CONFIG_NFC_ST21NFC) += st21nfc.o
3. Copy the st21nfc.* file into $KERNEL_DIR/drivers/misc. The I2C driver is of class misc.

## Slide 4: Kernel Integration – how to integrate driver into the kernel – Configure the kernel driver with DTS
4. Ensure that 2 GPIOs are assigned to the ST21NFCD device:
  An input reserved for the IRQ pin (Wake Up), associated to an interrupt with rising edge polarity.
  An output reserved for the Reset pin (RSTB). (active low reset )
5. In the board/reference platform start-up code file $KERNEL_DIR/arch/<your-arch>/boot/dts/<your-board>.dtsi, declare the st21nfc device by adding:
  st21nfc@08 {
    compatible = "st,st21nfc";
    reg = <0x08>;
    interrupt-parent = <&gpio >;
    interrupts = <gpio_nb_for_wakeup 0>;
    st,reset_gpio = <@gpio gpio_nb_for_reset 0x00>;
    st,irq_gpio = <@gpio gpio_nb_for_wakeup 0x00>;
    status = "ok";
  };
6. Enable the ST21NFCD in the specific defconfig file ($KERNEL_DIR/arch/<your-arch>/configs/<your_config>_defconfig) by adding the following line:
  CONFIG_NFC_ST21NFC=y

## Slide 5: Kernel Integration – how to integrate driver into the kernel – Check the ST21NFCD driver integration
If the ST21NFCD driver is correctly integrated: •
  After booting, the device node should be visible on the booted Android device. It can be checked within an adb shell. An instance should be returned with:
    ls -l /dev/st21nfc
  After booting, the GPIOs dedicated to the ST21NFC should be visible if you execute the following command on the booted Android device, within an adb shell:
    cat /sys/kernel/debug/gpio
  Kernel must be configured with CONFIG_DEBUG_GPIO=y.
Note:This check can be done even if the ST21NFCD is not connected to the platform.
Note:To ensure that the driver is properly integrated, inspect the GPIO and interrupts in /proc/interrupts.